## Slide 1: Development of an IM AF encoder
Author: Eugenio Oñate Hospital
Course: MSc FT Digital Music Processing
School of Engineering and Compute Science
Queen Mary University of London

## Slide 2: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 3: 1. Introduction
Music industry needs a revulsive, the sales still decreasing
Traditional formats are no longer attractive for costumers
Notes: 2. Music market is stuck. Customers need new products that attract their attention.
Digital files like MP3 were a good revulsive for the industry but have been here since 90s
This graphic shows how the sells are decreasing. Also, how each era has had its own file format.
Now is an exciting moment to innovate and create a new file format.
All those examples do not allow interactivity between the user and the music.

## Slide 4: 1. Introduction
At presents, technology has evolved so fast opening the door for new tools
People is connected among themselves sharing all kind of information
Music industry has been reluctant to let people interact with their songs
A new interactive music service has emerged
Future will be dominated by this new concept of digital music content
Notes: 2 .Using smartphones or tablets they connect to social networks like Facebook or Myspace.
This makes the perfect opportunity to change the way we listen the music,
Making the user participant of the experience
3. Because the technology was not ready.

## Slide 5: 1. Introduction
For its success, it is essential to have a standardize file format that can supply interoperability between different interactive services and music players.
This files is called Interactive Music Application Format
IM AF allows users to modify the volume of each instrument separately, select a mixing preset or share their creations
IM AF opens a new range of opportunities for the music sector
Web pages like Myspace or Last.fm will benefit from this file
Notes: 2. The moving picture experts group defines a new file format that Is part of the multimedia application format
3. IM AF is a versatile file format that allows …
4. Mixing preset: to change the mixing style according to some presets predefined by the producer.
5. Web pages like myspace or last.fm could use this new file instead the regular mp3 improving the user’s experience

## Slide 6: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 7: 2. Objectives
The main objective of the thesis has been to develop an encoder able to create an IM AF file
For this purpose a program in C has been written following the standard defined by MPEG.
The IM AF file allows users more control over the song. More specifically, it permits to vary the volume of each instrument or choose a predefined preset.
All the actions are supervised by rules, thereby protecting the initial intention of the author.
The performance of the encoder has been validated by creating three IM AF files with special features. These conformance files have been successfully tested in the IM AF player provided by the MPEG group.

## Slide 8: 2. Objectives
Technical features of the new encoder
The file will have the following characteristics:
    16 tracks maximum
    Sampling frequency of 44.1 kHz
    Bit rate of 128 Kbit/sec
    Resolution of 16 bits
  It will hold presets and rules
    Presets: predefined values of the volume of each track
    Rules: limitations imposed by the creator of the song
The encoder uses a simple command line user-interface to introduce data

## Slide 9: 2. Objectives
Background technology
Besides the implementation in C of the encoder, we will study the file structure of MPEG-4 and MPEG-1 Layer III
MPEG-4 is the bases of IM AF and MP3 is the supported file format of this encoder

## Slide 10: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 11: 3. Background research
MPEG-1 Layer III, MPEG-4 and previous interactive systems
  MP3 – Released in 1991
    Uses different techniques for audio compression -> Achieves high reduction of size with good quality
    Most used tool for internet and audio delivery
    Standard file format for the general public
    Works in mono, stereo or joint-stereo
    Standard sampling frequency is 44.1 kHz
    Bit rate responsible of the quality, from 8 Kbit/s to 320 Kbit/s
    Bit rate can be constant or variable
Notes: 6. Joint-stereo codes parts of the spectrum that human hear can not perceive as mono. Creates 2 channels one containing the information of both channels and the other the differences. Achieves efficient results in terms of saving space.
7. SF: but there are more options 23 kHz and 48 kHz
9. Variable bit rate permits higher bit rates for complex parts of the song while less space is saving for less complex parts

## Slide 12: 3. Background research
  MP3 file structure
    MP3 is split in small blocks of data or frames
    Each frame has 1152 samples / 44.1 kHz = 0.026sec
    If bit rate 128 Kbit/s -> 417 Bytes size each frame
    ID3 TAG: metadata containers of song information
    Each frame has 32 Bytes of header followed by samples
    Header contains technical information: Layer, bit rate, copyright, protection bit and more
[ID3 TAG] | Frame1 | Frame2 | ... | FrameN | [ID3 TAG]
Notes: 0. I’ll present the structure of mp3 because the encoder has had to read the mp3 file to extract the relevant information.
3 . Frame len = int (144*128000/44100)+1 = 417 Bytes
6. The header is used to find the beginning of the frame. Depending on the MP3 encoder the header may vary.
Some encoders add a protection bit others add a copyright bit...

## Slide 13: 3. Background research
MPEG-4 is an evolution of MPEG-2
  Main different: Object-based model
    It uses independent objects with connection in time and space
    Different type of data are integrated in the scene
  It does not focus on a single application
  File format defined for MPEG-4 is MP4
  MPEG-4 is an important part of the framework of the IM AF file
Notes: 1. Unlike its predecessors improving the compression methods was not the main task
3. Video, audio and images are stored together for conform a MPEG-4 file
4. App: It is used in every app that needs advance audio compression, synthesis or manipulation
  6. Its structure will be presented later together the IM AF

## Slide 14: 3. Background research
Previous interactive systems
iKlax Player
IEEE 1599
iXMF
Notes: Three examples are presented:
iKlax: produced in France, they propose a file format with separated tracks and interactivity to manipulate the piece.
The project includes a music player and a music editor.
It has two levels of interactivity: first level allows selection of tracks and the second level allows users modify the level of each track
- The image shows an example of an iKlax player.
IEEE 1599: Offers a new approach to interactive files. Combines in a single file music and XML symbols as graphical representation of music.
  The images shows the different sections of the file. General stores info about the piece. Logic the symbols. Structural classify musical objects and the connection. Notational : visual representation of the symbols. Performance is a computer-based description of the
  representation of the music. Audio is the digital recording.
iXMF or interactive extensible music format is created for video games industry.
  Includes in a single file all the information needed to perform the track. The same information defines the structure of the file
  iXMF stores the media chunks in Cues. This picture shows the different cues that an iXMF can store. The media folders the actions and levels.

## Slide 15: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 16: 4. Development of IM AF file
An interactive music file based on the new IM IF connects multiple tracks with related information under a well defined structure
Content: tracks, presets and rules
  Track: one or more instruments that can be stored in the file
  Preset: Pre-defined information related to the volume of each track
  Rules: Limitation on the user’s movements, for preserving the initial intention of the producer.
The created file is reproduced using an IM AF player

## Slide 17: 4. Development of IM AF file
IM AF usage mode and rules

## Slide 18: 4. Development of IM AF file
IM AF player
User mix
Preset mix

## Slide 19: 4. Development of IM AF file
File structure
Notes: 0. In the thesis I explain all the sections of the file in detail. Here I just going to do a brief summary of the relevant parts.
The file is composed of boxes. Those represent a section of memory in with information is stored.
Track – stores the particular information of each track. There will be as many boxes as number of instruments.
The encoder stores the media data in samples. This information is stored in the media data container. In order to reproduce these data, the encoder needs a series of tables relating time, offset and data of the media samples. Those tables are held inside the sample table box.

## Slide 20: 4. Development of IM AF file
File Type Box
  It specifies the brand identifier of the file
Notes: This table specifies the characteristics of the audio tracks that can be supported by the encoder

## Slide 21: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 22: 5. Implementation
The program has two parts:
  Main program
    Includes the functions needed to fill the boxes and write them in the binary file and read the data from the audio files (MP3)
  IM AF Encoder.h -> header
    Includes the definition of the boxes
The encoder converts the MP3 into MPEG-4 audio files.
  First step is to read the MP3 frame by frame and extract the samples.
  This conversion is made automatically each time the user enters a new instrument

## Slide 23: 5. Implementation
Samples are stored in the media data container

## Slide 24: 5. Implementation
In addition to samples, the encoder needs to extract sample information
Notes: So the decoder can reconstruct the audio files

## Slide 25: 5. Implementation
Steps for creating an IM AF file
  The encoder uses a simple command line user-interface for allowing user to enter the data.
  Step 1
  The number maxim of tracks is specified by the brand identifier of the File type box.
Notes: Step 1 : the user have to specify the number of instruments that he wants to enter.
3. In case the user enters a higher number, the encoder ask again for the information.

## Slide 26: 5. Implementation
Step 2
  In case the name is not found, the encoder asks again
Notes: Step 2 . Once the number is specified, he has to enter the names of each instrument.
1. The files must be in the same folder as indicated in the code. In case the user wants to add a file that is not there, the encoder won’t find it.

## Slide 27: 5. Implementation
Step 3 – Creation of the preset
Step 4 – Creation of the rules
Notes: Step 3 - When the user has finished to enter all names, the encoder creates the preset defined previously in the code. To provide clarity on what is being writing in the file, the encoder prints on screen the characteristics of the preset.
Step 4 - Finally, last step is to write into the file the rules. They are also written directly in the code rather than using the command line. But the encoder shows the different rules implemented

## Slide 28: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 29: 6. Results
Three examples have been created for validation of the IM AF encoder
Example 1: Acoustic song
Notes: The objective of this thesis is to create an encoder able to generate IM AF files. To demonstrate its operation, three different files were implemented.
Each conformance file presents different configurations of the encoder parameters

## Slide 30: 6. Results
Example 2: Electro song

## Slide 31: 6. Results
Example 3: Rock song

## Slide 32: 6. Results
Advantages of the new IM AF encoder
  Intended for all users
    Beginners will find it useful and intuitive
    Command line interface guides the newcomer through the creation of the file
    As the user gets confidence is very simple to customize the encoder
    Written in C -> classical environment
    Experimented user will find it sufficiently robust for his/her work.
    Flexible enough to support changes
Notes: Advantages of the encoder
1.From beginners until professionals.
2. Beginners: because they do not need to modify the code to create a new IM AF file
4. C: and very easy to understand. It does not use any external libraries.
5. Robust thus making it easy to make the encoder a professional tool. In case the user wants to introduce new improvements the encoder is.. .

## Slide 33: 6. Results
Advantages of the new IM AF encoder
  Very efficient: works with long audio files (5/6 minutes or +)
  Open them, extract the info and merge it all inside the file in less than a minute.
  The lightness of the encoder makes it suitable for applications that work in low processor environments
  Supports MP3 -> minimize the size in bytes of the IM AF file
    Important because when working with separate tracks the size tends to increase

## Slide 34: 6. Results
Weakness
    The command line interface is limited
    Preset and rules information must be written directly in the code
    The user must install a C editor for compiling the code
    Compatibility of audio files: just MP3
    The tracks must be in the same folder as indicated in the path. If not, the encoder will not find the tracks.
    I does noy supports images and synchronized text
Notes: 3.rules: Rather than using the command line
5. The user must convert all his songs to MP3 . There are a lot of free software that does the conversion
6. Those aspects would have been incorporated with more time

## Slide 35: Content
Introduction
Objectives
Background research
Development of IM AF file
Implementation
Results
Conclusions

## Slide 36: 7. Conclusions
We have created an encoder for IM AF files
The code is divided in two parts:
  IM AF Encoder.h : generates the framework of the file
  Main.c fills this framework with the data needed and writes the binary file
The conversion and processing of MP3 has been a fundamental part in the success of the encoder
The encoder uses C as the programming language
Three examples are presented
Notes: MP3: for doing that we have studied the standard to understand how an MP3 works. The creation of an encoder needs an exhaustive control over the data
thats why the encoder….
C is a complete but basic language that does not incorporate external libraries.
Ex: they prove the compatibility and the correct operation of the encoder

## Slide 37: 7. Conclusions
This thesis has helped me to improve my programming skills.
Also, I have become familiarized with a new and promising technology – IM AF
Main obstacles:
  Understand the file format from the ISO and how I would implemented.
  Find the best suitable code and programming techniques
  Eliminate artifacts produced by the wrong manipulation of samples

## Slide 38: 7. Conclusions
Future work
  Ability to store images like the album’s cover and pictures
  Insert synchronized text for karaoke
  Store tracks online to let users share their instruments
  New tools:
    Equalized for each channel
    3D panorama – placing each track in a different position of the space
  Technical part: Translate the code to C++ or Java
Notes: 0. Despite the encoder created in this thesis does its task properly, time limitations have prevented the implementation of some interesting additional tools.
3. instruments: without the need to have physically the file
4. EQ: to have the chance of manipulating the frequencies
5. 3D : the user would move the instrument in the 3D space,
6. To make the encoder suitable for mobile applications

## Slide 39: END
Many thanks for your attention
Any question?
                Eugenio Oñate