## Slide 1: MAP computer model of the auditory periphery
Ray Meddis
University of Essex, UK
rmeddis@essex.ac.uk
Notes: <number>

## Slide 2
BM motion
IHC stereocilia
receptor potential
transmitter release
auditory nerve
action potentials
pure tone stimulus
stapes
Brainstem response
<number>
Stages of peripheral hearing
Notes: <number>

## Slide 3: What is a computer model?
A model is a set of equations representing the physiological transformations of the signal between the eardrum and the brainstem
The equations are arranged in a cascade so that the output of one is used as the input of the next in the sequence
The equations and the parameters are all published and regularly improved
Notes: <number>

## Slide 4: Downloadable
The software is free and can be downloaded across the internet
  http://www.essex.ac.uk/psychology/psy/PEOPLE/meddis/webFolder10/WebIntro.htm
programming language is MATLAB
software comes as a folder to drag and drop
Notes: <number>

## Slide 5: Example output
<number>
Notes: <number>

## Slide 6: Demo programs
Notes: <number>

## Slide 7: MAP demo single channel BF= 1 kHz
stapes
BM
IHC receptor potential
IHC/ AN synapse
AN spikes
cochlear nucleus chopper
inferior colliculus chopper
Notes: <number>

## Slide 8: MAP demo multi-channel model
stapes
BM
IHC receptor potential
IHC/ AN synapse
AN spikes
Notes: <number>

## Slide 9: MAP speech demo
‘107’
(one oh seven)
stapes
BM
IHC receptor potential
IHC/ AN synapse
AN spikes
Notes: <number>

## Slide 10: Multi-channel model 2-tone suppression example
Notes: <number>

## Slide 11: Module sequence
1. stimulus
2. stapes
3. BM (4. IHC stereocilia)
5. IHC receptor potential
6. IHC/ AN synapse
7. AN spikes
8. CN chopper or primary-like
9. IC chopper or primary-like
Notes: <number>

## Slide 12: Practicalities
Notes: <number>

## Slide 13: Running the model
1. Generate the input signal
  inputSignal=zeros(1, 1000)
  inputSignal(50)=1; % click
  inputSignal=amp*inputSignal; % specify signal in µPa
2. Specify parameters
  method=MAPparamsDEMO(BFlist, sampleRate);
  method=plotGraphs=1;
3. Identify the modules to be used
  moduleSequence= [1 :7 ]; % up to auditory nerve
4. Run the module
  [earObject, method, A]=MAPsequenceSeg( inputSignal, method, moduleSequence);
Notes: <number>

## Slide 14: Parameter files (normal, impaired parameters supplied)
function method=MAPparamsDEMO(BFlist, sampleRate, showParams)
% module #1 inputStimulus
inputStimulusParams=[]; % clear the structure first
inputStimulusParams.sampleRate= 1/method.dt;
inputStimulusParams.boundaryValue=[];
% module #2 outerMiddleEar
outerMiddleEarParams=[]; % clear the structure first
outerMiddleEarParams.stapesScalar= 6e-008;
outerMiddleEarParams.dt= -1;
outerMiddleEarParams.filters= [0 900 2];
% module #4 IHC_cilia
IHC_ciliaParams=[]; % clear the structure first
IHC_ciliaParams.tc= 0.0003;
IHC_ciliaParams.C= 0.1;
IHC_ciliaParams.Gmax= 8e-009;
IHC_ciliaParams.Gu0= 1.974e-009;
IHC_ciliaParams.u0= 7e-009;
IHC_ciliaParams.s0= .25e-007;
IHC_ciliaParams.u1= 7e-009;
IHC_ciliaParams.s1= 10e-009;
IHC_ciliaParams.u0= 40e-009;
IHC_ciliaParams.s0= 1.e-007;
IHC_ciliaParams.u1= 7e-009;
IHC_ciliaParams.s1= 20e-009;
% module #5 IHC_RP
IHC_RPParams.Cab= 16e-012; % IHC capacitance (F)
IHC_RPParams.Et= 0.11; % endocochlear potential (V)
IHC_RPParams.Gk= 1.8e-008; % potassium conductance (S)
IHC_RPParams.Ek= -0.0705; % potassium equilibrium potential
IHC_RPParams.Rpc= 0.04; % combined resistances
% module #6 IHCpreSynapse
IHCpreSynapseParams.GmaxCa= 8e-009; % maximum calcium conductance
IHCpreSynapseParams.ECa= 0.066; % calcium equilibrium potential
IHCpreSynapseParams.beta= 400; % parameters determining channel opening
IHCpreSynapseParams.gamma= 130; % parameters determining channel opening
IHCpreSynapseParams.tauM= 0.0001; % membrane time constant
IHCpreSynapseParams.tauCa=tauCas; % calcium clearance (LSR first)
IHCpreSynapseParams.power= 3; %
IHCpreSynapseParams.z= 2e42; % scalar Ca -> vesicle release rate
% module #7 AN_IHCsynapse
AN_IHCsynapseParams.mode= 'spikes';
% AN_IHCsynapseParams.mode= 'probability'; % faster
AN_IHCsynapseParams.M= 12; % maximum number of vesicles in available store
AN_IHCsynapseParams.y= 3; % rate of replacement of lost vesicles (vesicles/s)
AN_IHCsynapseParams.y= 10; % rate of replacement of lost vesicles (vesicles/s)
AN_IHCsynapseParams.l= 2580; % rate of loss of vesicles from the cleft
AN_IHCsynapseParams.x= 30; % rate of replenishment from the re-uptake store
AN_IHCsynapseParams.r= 6580; % rate of reuptake from the cleft into the cell
AN_IHCsynapseParams.refractory_period= 0.00075;
AN_IHCsynapseParams.PSTHbinWidth= 0.001;
Notes: <number>

## Slide 15: Brainstem units
Notes: <number>

## Slide 16: Adding brainstem units
AN CN chopper IC chopper
Different kinds of brainstem units can be used
(e.g. primary-like, pauser, build-up
Notes: <number>

## Slide 17: MAP demo with brainstem units
stapes
BM
IHC receptor potential
IHC/ AN synapse
AN spikes
cochlear nucleus chopper
inferior colliculus chopper
Notes: <number>

## Slide 18: Latest news: efferent system
Notes: <number>

## Slide 19
BM motion
IHC stereocilia
receptor potential
transmitter release
auditory nerve
action potentials
pure tone stimulus
stapes
Brainstem response
<number>
MOC
efferents
acoustic
reflex
New feedback loops
Notes: <number>

## Slide 20: Doing psychophysics
The first step is to get the model to make decisions
Threshold decisions
  did you hear it?
Notes: <number>

## Slide 21
Stimulus is above threshold if at least one spike occurs
<number>
Notes: <number>

## Slide 22: Psychophysical evaluation of the model
experimenter model
model makes the decisions and presses the buttons
<number>
Notes: <number>

## Slide 23: Forward masking paradigm
Notes: <number>

## Slide 24: iso-forward masking contour (IFMC)
8 ms
2 kHz
10 dB SL
Vary masker frequency
masker level
masker probe
108 ms
variable
frequency
10 ms gap
<number>
Notes: <number>

## Slide 25: TMC (temporal masking curve)
masker probe
2 kHz 2 kHz
variable gap
<number>
Notes: <number>

## Slide 26
100
1000
10000
-
100
1000
10000
model (CMa) data
Notes: <number>

## Slide 27: Thank you!
Notes: <number>

## Slide 28: Multi-channel brainstem model
BF1
BF2
BF3
AN CN chopper IC chopper
Notes: <number>